## Slide 1: ExaO: Software Defined Data Distribution for Exascale Sciences
CERN,
California Institute of Technology,
Yale University

## Slide 2: The Compact Muon Solenoid Computing Model
Large raw datasets from LHC at the Tier-0 site
RECO and AOD datasets are distributed to Tier-1 sites
RECO, AOD and simulation datasets are transferred among Tier-1~3 sites for analysis.
Event Summary Data(ESD): ~1MB/evt
Analysis Object Data(AOD):~100kB/evt
Derived Data(dESD,dAOD,NTUP,...)

## Slide 3: PhEDEx: CMS Data Transfer Service
Number of files > 63 million
Average file size 2.6GB
Total volume
> 160PB
Dataset hundreds to thousands files
Dataset transfer requests
400-500 per day
Multiple transfer patterns:
one-to-one,
one-to-many
many-to-one
Users submit requests through web interface
Central data movement decision based on history statistics
Automatic Data Management and Movement in CMS

## Slide 4: Limitation of PhEDEx
Built on top of traditional multi-domain networks
Inflexible, static dataset level scheduling
Performance
● Inflexible infrastructures
● Lack of real-time, global network view
● Infeasible of end-to-end data flow orchestration
● Traditional client/server mode to select source for all files at once
● Complete ignorance of destination sites’ potential as file providers
● No network resource allocation scheme
  ● Low concurrency
  ● Low link utilization
  ● Long transfer delay

## Slide 5: Example: Distributing Dataset X to All the Sites in PhEDEx
Only site 1 is considered as a potential source
PhEDEx scheduling: site 1 sends all 3000 files to each destination
  (File K, site 1, site X) where K=1, 2, …, 3000 and X=2, 3, … 7
  Low concurrency
Only the uplink of site 1 is utilized and becomes the bottleneck
  Low link utilization:
Flows compete for network resources
  With TCP, the fair share of each site-to-site flow converges at 100/6=16.7Gbps
Dataset X (3000 50GB files)
Bottleneck
CMS Needs A More Efficient, Flexible Data Transfer Service

## Slide 6: Design Challenges for An Flexible, Efficient Data Transfer Service
Challenge 1
Challenge 2
Challenge 3
Provision of a global,
real-time, inter-domain
network view
Flexible, dynamic scheduling with high transfer concurrency
Efficient orchestration among end-to-end data flows with high network resource utilization
Solution?
ExaO: A Software Defined Data Transfer Orchestrator

## Slide 7: ExaO: Software Defined Data Transfer Orchestrator
PhEDEx
Dataset level scheduling
Destination sites cannot become candidate sources until receiving the whole dataset
Low concurrency
Scheduler
Centralized, dynamic, network-aware file level scheduling
Leverage destination sites as candidate sources after file reception
High concurrency
No network resource allocation scheme
Data flows compete for network resources
Low utilization
Scheduler and Transfer Execution Nodes (TEN)
Global, dynamic rate allocation among data flows (Scheduler)
End host rate limiting to enforce allocation (TEN)
ExaO
No real-time, global network view
Application-Layer Traffic Optimization (ALTO)
Collect complete network state at different domains (OpenDaylight)
Compute real-time routing information at different domains (ALTO-SPCE)
Compute global, on-demand, minimal, equivalent abstract routing state (ATLO-RSA)
Notes: Minimally invasive change on end host groups
Real-time, dynamic resource allocation under the existence of other network traffic
Not CMS or HEP specific, hence support any data intensive sciences.
Dataset distribution to N destination:
  Maximal link utilization in the testbed
  N times faster than dataset level scheduling

## Slide 8
Components of ExaO
RESTful-API
allow users submit and manage transfer request through different interface
ALTO
collect on-demand, real-time, minimal abstract routing information
ExaO Scheduler
centralized, efficient file-level scheduling and network resource allocation
FDT
efficient data transfer tools on end hosts
Monalisa
Distributed monitoring infrastructure for real time monitoring of each flow, transfer
Transfer Execution Nodes
enforce scheduling and rate allocation decisions at end hosts
enforce resource allocation in the network

## Slide 9: ExaO Workflow
Users submit, track and manage dataset transfer requests
User Requests

## Slide 10: ExaO Workflow
Users submit, track and manage dataset transfer requests
Scheduler queries NEW requests via ExaO RESTful interface
Scheduler queries ALTO controllers for routing state
Routing Query
Routing Query
Routing Query
User Requests

## Slide 11: ExaO Workflow
Users submit, track and manage dataset transfer requests
Scheduler queries NEW requests via ExaO RESTful interface
Scheduler queries ALTO controllers for routing state
ALTO controller collects complete network state and computes on-demand, minimal, abstract routing state in response to query
Routing ACK
Routing ACK
Routing ACK

## Slide 12: ExaO Workflow
Users submit, track and manage dataset transfer requests
Scheduler queries NEW requests via ExaO RESTful interface
Scheduler queries ALTO controllers for routing state
ALTO controller collects complete network state and computes on-demand, minimal, abstract routing state in response to query
Scheduler makes centralized, dynamic, file-level scheduling and global network resource allocation decisions
Schedule Decisions
Schedule Decisions
Schedule Decisions
Schedule Decisions

## Slide 13: ExaO Workflow
Users submit, track and manage dataset transfer requests
Scheduler queries NEW requests via ExaO RESTful interface
Scheduler queries ALTO controllers for routing state
ALTO controller collects complete network state and computes on-demand, minimal, abstract routing state in response to query
Scheduler makes centralized, dynamic, file-level scheduling and global network resource allocation decisions
Transfer Execution Nodes (TEN) query updated scheduling and allocation decisions
TEN instruct efficient data transfer tools on end hosts (e.g., FDT) to enforce scheduling and allocation decisions
TEN Query
TEN instruction
TEN instruction
TEN ininstruction
TEN instruction

## Slide 14: ExaO Workflow
Users submit, track and manage dataset transfer requests
Scheduler queries NEW requests via ExaO RESTful interface
Scheduler queries ALTO controllers for routing state
ALTO controller collects complete network state and computes on-demand, minimal, abstract routing state in response to query
Scheduler makes centralized, dynamic, file-level scheduling and global network resource allocation decisions
Transfer Execution Nodes (TEN) query updated scheduling and allocation decisions
TEN instruct efficient data transfer tools on end hosts (e.g., FDT) to enforce scheduling and allocation decisions
MonALISA sensors monitor data transfer status and send update back
Transfer Status
Transfer Status
Transfer Status

## Slide 15
Minimally invasive change on end host groups
Not CMS or HEP specific, hence support any data intensive sciences
Real-time, dynamic resource allocation under the existence of other network traffic
Dataset distribution to N destination
Maximal link utilization in the testbed
N times faster than dataset level scheduling
Practical Concerns

## Slide 16: Example: Distributing Dataset X to All the Sites in ExaO
Site 1 is the only source at the beginning
Each site can become a file provider once receiving files
Site 1 sends 3000/6=500 unique files to each destination site
  Limit the rate of each (site 1, site X) flow as 100/6=16.7Gbps
  Uplink utilization: 100%
Site X (X=2, 3, …, 7):
  becomes a source to other destination sites after receiving a unique file from site 1
  sends the received file to all other 5 destination sites, each at (100-16.7)/5=16.7Gbps
  Uplink utilization: is 83.3%
Total link utilization: 6/7=85.71%
  6 times of PhEDEx
  Maximum
Dataset X (3000 50GB files)

## Slide 17
A user submits a request:
  {
  “DatasetName”: “A”,
  “Destination”: {“Site 2”, “Site 3”, “Site 4”, “Site 5”, “Site 6”, “Site 7”}
  }
ExaO receives this request and makes online file-level scheduling to maximize network utilization
Audience observe the scheduling decision made by ExaO and the high link utilization from testbed UI, and observe the status of file transfers through Monalisa
Demo:

## Slide 18: Thank You!