## Slide 1: Supercomputing 2016 Network Architecture and Demonstrations
Version: 11/3/16

## Slide 3
WAN and Inter-booth Connections

## Slide 4
PRP WAN Connections
Los Angeles
3 x 100GE links at 818 Los Angeles
  Shared among CENIC connected sites
1 x 100GE (600->818) Los Angeles
  Dedicated for Caltech
Sunnyvale
3 x 100GE links
  Shared among (UCSC, CENIC perfSONAR)
  Other campuses …
Layer2 Infrastructure
  6 Vlans

## Slide 5
Booth Connections
All the connections to booths are through the OTN Metro DCI Connections
1Tbps Booths
  Caltech Caltech
  Caltech StarLight
  SCinet
100GE Booths
  UMich
  Vanderbilt
  SDSC
  Dell
  2CRSi
  Ethernet Alliance
Connections
  5 x WAN
  7 x Dark Fiber
  2 x 1Tbps

## Slide 6
Connection to Brazil
100G dedicated connection to FIU
FIU connects to ANSP and UNESP at 100G from Miami
100G Demonstration Plans
Caltech-FIU Network to Network
Caltech-UNESP
  Network – Network
FIU to Compute Canada
via StarLight

## Slide 7
List of Demonstrations

## Slide 8
SDN
  Infrastructure at SC fully programmable using the SDN controller
  Flow installation using:
    Operator view (full control on infrastructure)
    Science applications (done by the ALTO engine)
  Science DMZ Flow programming using BRO
  Rapid application development for Networkers / Scientist
Physics Applications
  Virtual Reality for CMS detector/beams View
  Machine Learning for CMS data
DTN Throughput
  PRP 100GE Disk to Disk (DTN to DTN)
  PRP 100GE Network to Network
NVME over Fabric among DTNs
  Single Server 200Gbps file transfers
1 Tera bps demos
  RDMA (RoCE) among a pair of server
  TCP/IP based among 4 systems

## Slide 9
Kibana Monitoring
Kibana Monitoring
ExaO
Rest Interface
ExaO
Rest Interface
ExaO
Rest Interface
DB
Kibana Monitoring
Monalisa
ExaO
Rest Interface
ExaO
Rest Interface
Scheduler
ExaO
Rest Interface
ExaO
Rest Interface
Transfer Execution Nodes
FDTDaemon
FDTDaemon
FDTDaemon
MLSensor
MLSensor
MLSensor
Phedex
ASO
Batch
ALTO
ExaO: EXAscale Data Transfer Orchestrator

## Slide 10
End-to-end orchestration of data flows involving multiple host groups at different domains,
  RESTFul-API: allow users submit and manage transfer request through different interface
  ALTO: collect minimal, real-time network information from different domains
  ExaO Scheduler: centralized, efficient file-level source and rate co-scheduling
  FDT: efficient data transfer tools on end hosts
  Monalisa: Distributed monitoring infrastructure for real time monitoring each flow, transfer
Minimally invasive change on end host groups
Real-time, dynamic resource allocation under the existence of other network traffic
Not CMS or HEP specific, hence support any data intensive sciences.
Dataset distribution from one site to N sites:
  ~100% link utilization in the testbed
  N times faster than dataset-level transfer scheduling
ExaO: EXAscale Data Transfer Orchestrator

## Slide 11: New Tools
Powerful state of the art, generic tools to substantially simplify SDN programming
Before (low level programming)
Low-level, complex OpenFlow rule programming
Programmer can define only at flow level
Specific access control allowing only hosts partition
Maple programming (high-level programming)
High-level, completely south-bound agnostic, cross-layer programming
Programmer sees (logically) each and every packet
Integrated access control supporting per-user or role based programming
FAST (automation function store)
Automatic execution dependency tracking
Automatic cleanup, re-execution (intent ++)
Host generic network functions
Before (raw data store)
Complex, manual tracking of execution dependency
Manual cleanup, re-execute
Designed directly on raw data store
Data Store
Before (manual programming)
Complex, manual maven programming
Web IDE
Web-based automatic generation of projects
Programmer focuses only on key aspect
Before
Ad hoc flow rule installation
FAST Schedule
Consistent, optimized flow-mod scheduling

## Slide 12: High-level SDN Programming Abstraction: Function Store (Details; skip)
function instance
public void QoSRouting(Ipv4Address src, Ipv4Address dst, int requiredBw) {
srcNode, dstNode = mapToNode(src, dst);
topology = readTopology();
pq.add(srcNode);
while (!pq.isEmpty()) {
n = pq.pop();
if (bw_src(n) < requiredBw)
return failure
if (n == dstNode)
return writeRoute(src, dst, path);
for (e(n->m): n.neighbors) {
if (min(e.bw, bw_src(n)) > bw_src(m)) {
updateBw(m, min(e.bw, bw_src(n)));
...
}
}
}
return failure }
    Allow generic functions
    Automatically track data dependency
    Automatic clean up, reschedule, and re-execute after dependent data changes (achieve intent)
function instance
function instance

## Slide 13: High-level SDN Programming Abstraction: Maple Programming (Details; Skip)
Consider each pkt as a request
- Network as a single virtual server
- Network functions (logically) invoked on each new pkt, returning how net handles that request
- Network functions expressed in general purpose language
- Realization of return is opaque, computed by system

## Slide 14: Example Maple Program
void f(Packet p) {
if ( !permit(p) ) p.route = null;
else {
EndpointProp sedp = hostTable(p.ip.ipSrc());
EndpointProp dedp = hostTable(p.ip.ipDst());
int rate = p.te.vRate(); // custom protocol
QoSRoute qr = routingAlg(sedp, dedp, rate);
p.route = qr.route; p.vrate = qr.rate;
}
}
QoSRoute routingAlg(EndpointProp s, EndpointProp d, int r) {
if ( allowedRate(s, d) < r ) // authorization
r = allowedRate(s, d);
return QoSRouting(s, d, r);
}
Per-packet programming model
Standard+Custom protocols
Meta header to control cross layers
Unspecified realization: Source-routing, compile, or on-demand at switches
Notes: relatively low rate, unreliable, nodes are highly mobile

## Slide 15: IDE Features (Details, with a screenshot, use callout to label key components/features; Skip)

## Slide 16
New Tools in Action: Programmable Science DMZ
Bro
function cloud
Bro
Bro
transport network
RESTCONF /YANG Data Store
Data-driven function/transport control
TO FINISH

## Slide 17
New Tools in Action: Programmable Science DMZ
Network
Bro
SDN Controller
TAP
Control on data and tapped data
Tapped data controlled using SDN flow programming
Highly selective control to avoid Bro becoming a bottleneck
Flexible, generic mechanisms to program the complete system Three control points
What to tap and how to control it ? SDN programming model
How to notify from Middlebox to the SDN controller? (RESTCONF to modify SDN data store)
How to adaptively control the tapping and the original data?
How to program the Middlebox to achieve flexible programing (Bro’s programming model)
State updates (RESTCONF/YANG data store as standard interface)
FAST (programming approach) to make controller program state transition oblivious
Incremental vs lambda programming

## Slide 18
Programmable DMZ using FAST Maple
Flexible, stateful firewall programmed using Bro
  Up to Layer 7 detection
Generic FW state update to SDN controller using RESTCONF
SDN control programming using Maple programming, executed in FAST function store
Achievements: only 10s of lines code, for a fully adaptive, highly extensive ScienceDMZ

## Slide 19
1Tbps Caltech-StarLight (among two booths)
SCinet has provided DCI inter-booth connection with a total of 8 x 100G links
RoCE based data transfers
A proof of concept to demonstrate the current system capability and

## Slide 20
1Tbps Caltech - Caltech
Cisco has provided DCI inter-booth connection with a total of 10 x 100G links
Transfer Application:
FDT: TCP/IP based application for data transfers

## Slide 21: Traffic monitoring
OpenFlow STATS
sFLOW (inmon)
Maddash

## Slide 23: FASTMapleNet: Easy-to-Program SDN Network for Scientists and Beyond
Powerful state of the art, generic tools to substantially simplify SDN programming
  FAST function store
    Automatic track execution dependency.
    Automatic cleanup, re-execute, schedule network services (intent ++)
    Host generic network functions
  Maple programming as "omnipresence" programming
    Programmer sees (logically) each and every packet
    High-level, completely south-bound agnostic
    Integrated access control supporting per-user or role based programming
  Web based IDE
    Simplest approach to achieve a science problem

## Slide 24
Programmable DMZ using FAST Maple