## Slide 1: Toward Super High-Level SDN Programming
Joint project of Caltech, Tongji, Yale
May Wang
Nov. 16, 2016
Notes: we are now collaborating with Caltech along with some most successful companies to operate a 100Gbps SDN network (photos here)

## Slide 2
Notes: We know that super computing depends very much on the support from super network. And what we do is to design and implement super or say, high performance network. To be more specific, what do we do?

## Slide 3: Issues in Current SDN Programming
Issue 1: SDN programmers manually write Openflow rules; Openflow is a low level and limited computation model
Openflow does not support logic negation, and hence needs priority to simulate logic negation;
Openflow supports only layer 2 to layer 4, but many decisions depend on higher layers
For more information, please contact us: supersdnprogramming@gmail.com
Notes: Well, in the network field, we now pay attention to SDN, which is, software defined network, that allows people to define and manage the network by writing code. ( I remember Professor Harvey from Caltech also mentioned this in yesterdays presentation. ) In this way, we can realise the central control of the whole network and don’t need to update the functions by buying new machines, however, we can write code to achieve that.
However, there are still several problems.
First, SDN programmers have to manually write openflow rules which is a low level and limited computation model.

## Slide 4: Issues in Current SDN Programming
Manual data tracking leads to a bug in basic system service.
This code is from the l2switch project in ODL
For more information, please contact us: supersdnprogramming@gmail.com
Issue 2: SDN programmers manually setup listeners for data changes and handle data change events
Notes: Second, programmers need to manually setup listeners for data changes and to handle data change events
L2 switch project
2 parts:
Setup data change listener;
Implement ondadatachange function
Second part will never run

## Slide 5: Issues in Current SDN Programming
Issue 3: Complex, manual project lifecycle management.
The state-of-the-art SDN controller is OpenDaylight, OpenDaylight programming requires:
Handle project dependencies (feature.xml …)
Feature/Kar install in karaf console
•••
For more information, please contact us: supersdnprogramming@gmail.com
Notes: Third, programmers have to face the complex, manual project deployments.
(You don’t know how much time one programmer have to spend on deployment, seriously.)

## Slide 6: What is Our Solution?
Low-level, complex, limited (L2-L4) OpenFlow rule programming
Programmer can define only at flow level
Specific access control allowing only hosts partition
Complex, manual tracking of execution dependency
Manual cleanup, re-execute
Designed directly on raw data store
Complex, manual maven programming
High-level, completely south-bound agnostic, cross-layer (L2-L7) programming
Programmer sees (logically) each and every packet
Integrated access control supporting per-user or role based programming
Automatic execution dependency tracking
Automatic cleanup, re-execution (intent ++)
Host generic network functions
Web-based automatic generation of projects
Programmer focuses only on policy decision.
Manual programming
Low level, limited programming model
Raw data store
Web-based Integrated Dev Env (IDE)
Maple
FAST
Notes: Well, you will say, so many problems, does SDN programming really work? or is it just a concept, a game?
We deploy the system to solve the problems above and we have, indeed, and successfully deployed it on the real switches ( over there ) Yes it really works!

## Slide 7
Consider each pkt as a request
- Network as a single virtual server
- Network functions (logically) invoked on each new packet, returning how net handles that request
- Network functions expressed in general purpose language
- Network decision can depend on L2 to L7
Maple: High-level SDN Programming Language
For more information, please contact us: supersdnprogramming@gmail.com
Notes: To solve the first problem, we provide a programming model, called Maple.
Using Maple, you don’t need to be frustrated by the low level protocol, you write java code, to tell the switches, in this case, how you want the packet to be sent. And Shooo, it will follow your instruction to go there.

## Slide 8: Example
1. private static final String[] H12_TAP = { H1, "openflow:1:2", "openflow:2:1" }​
2. private static final String[] H12_ONE = { H1, "openflow:1:2", "openflow:2:3", "openflow:4:1" }​
3. private static final String[] H12_TWO = { H1, "openflow:1:3", "openflow:3:2", "openflow:4:1" } ​
4.​void f(Packet pkt) {​
5. int srcIP = pkt.srcIP(); int dstIP = pkt.dstIP();​
6. String flowId = computeFlowId( srcIP, dstIP, pkt.srcPort, pkt.dstPort, pkt.protocol );​
7. if ( srcIP == H1 && dstIP == H2 ) {​
8. FlowMetadata fm = getFlowMetadata(flowId); ​
9. if ( fm == null ) { ​
10. pkt.addRoute( H12_TAP );​
11. pkt.addRoute( H12_ONE );​
12. } else if ( isScience( getFileName( fm ) ) ) {​
13. pkt.addRoute( H12_TWO );​
14. } else pkt.addRoute( H12_ONE );​
15. } else if ( srcIP == H2 && dstIP == H1 ) {​
16. …​
17. } else pkt.addRoute( Route.drop );​
18. }​
Per-packet
programming
model
South-bound
agnostic
Control packets with L7 info
Network control based on high-level science data info
For more information, please contact us: supersdnprogramming@gmail.com
Notes: Consider this maple application example which wants to …
Maple app is a lamda function which is not increment function. What if the data changes, … (introduce FAST)

## Slide 9: Seamless L2-L4 to L7
For more information, please contact us: supersdnprogramming@gmail.com
If an MapleApp accesses L7 flow info (e.g., file name), system automatically sets up L7 inspection to extract info
Controller
Bro
FlowMetadata
MapleApp { … pkt.flow.fname }
Network
Setup path to tap traffic to Bro
A packet coming in
How to change the path automatically when FlowMetadata updated?
Network Monitor Framework
Setup Bro function
Flow (L7) info
Notes: To transfer application written by high-level language to low-level flow rules, we design the maple system. the maple system provides a per-packer …which conceptly process every-packet in the network.

## Slide 10: FAST: Function Automation System
Hosting generic data-driven network functions
  Easy-to-use programming paradigm
Automatic dependency management
  Track fine-grained runtime dependency
  Subscribe to data changes automatically
Enforced data consistency
  Rollback outdated function instances
  Re-execute to keep system state up to date
Generic Network Function
Function Instance Store
Data Store
Network
Data Read/Write
State update
Listener sub
Add/Remove
FAST
For more information, please contact us: supersdnprogramming@gmail.com
Notes: To solve the second problem, we provide FAST, that it can automatically manage the resources, dependencies, to keep the consistency. You may not understand how complex it is for SDN programmers to adjust the dependencies, but if I mention it can automatically keep the consistency, I believe all of you will understand how important it is.…
When state changes, …

## Slide 11: Web SDN IDE
Controller management
One-click deployment
Development and debugging
Topology and routes management
Network simulator
Connect to multiple controllers
Monitor controller state
Automatically generate Mininet topology scripts
Simplify the deployment process
Write Maple application
Check the TraceTree for debugging
Show topology
Check routes and flow tables
For more information, please contact us: supersdnprogramming@gmail.com
Notes: Also, we provide the SDN IDE, which is much more powerful than usual IDEs. Not only to write SDN codes, you can also test them by graphically creating a network environment, in our IDE. You can directly deploy the code by clicking a button, instead of spending a lot of time to fight with ODL, which is a super complex SDN platform for programmers.

## Slide 12: Summary: New Super SDN Programming Tools
Web SDN IDE: Dev, Op, User interfaces
Maple Runtime: Record the operations (read which fields) on packets and generates rules
Network Information Base: Provide network state, southbound driver
FAST: Track runtime data dependence & re-execute when data changes happen
Maple Lib: Read pkt fields, add route
MapleApp: A program written by java
System
User Programmer
Openflow Switch
Openflow Switch
Openflow Switch
Network
For more information, please contact us: supersdnprogramming@gmail.com
Notes: Therefore, to resolve these issues, we designed a series of tools to simplify sdn control programming.
Control space

## Slide 13: DEMO: Control Traffic based on L7 (HTTP Info)
S1
S4
S3
S5
Client (sc6)
Server (sc8)
Bro (sc9)
Controller
MapleApp.java
http.bro
Step of Demo:
1. User writes & deploys MapleApp program in Web IDE.
  Bro is a network monitor framework, in which we can get HTTP info for flows.
2. Client sends a request for science data at the Server.
  System generates a path to forward the traffic to Bro to get HTTP info (also forward the traffic to Dst by a default path).
3. Client sends a request for other type data at the Server.
S2
Client requests for science data (based on the info by file name in HTTP)
Path: S1  S4  S5
Path: S1  S2  S3  S5
TRUE
FALSE
  Bro will update the controller with the HTTP info.
  System will compute the correct path based on HTTP info.
For more information, please contact us: supersdnprogramming@gmail.com

## Slide 14: Thank You