## Slide 1: Toward Super High-Level SDN Programming
Yale University
Nov. 14-17, 2016

## Slide 2: Challenges
OpenFlow is a low level, complex computation model. However…
Complex manual tracking of execution dependency
Manual cleanup, re-execute
Data Plane
Control Plane :
Flow table
OpenFlow
Network State
Net Elem Datapath
Declarative Policy
Net Elem Datapath
logically centralized data store
programming to fill the gap
Challenge1:
Challenge 2:
Notes: 1.Complex, split programming model
(OpenFlow is a low level, complex computation model: it does not even support logic negation, and hence needs priority to simulate logic negation, it supports only layer 2 to layer 4, but many decisions may depend on higher layers )
2.Network dynamics(Complex manual tracking of execution dependency Manual cleanup, re-execute)

## Slide 3: Our Solution(New SDN Programming Tools)
WebIDE
FAST
Real Switch
Real Switch
Maple
Simple SDN
programming environment
Hight-level programming
Automatic data dependence and re-execute
Old SDN programming Modal
Switches
Ops Level
Under the hood
Controller Library
Step 1. Make Decisions
Step 2. Generate Rules
Step 1. Make Decisions
OF Switches
OF Controller Library
Step 2. Generate Rules
Ops Level
Under the hood
Super High-level SDN programming Modal

## Slide 4: WebIDE(Simple SDN programming environment)
Web-based automatic generation of projects
Programmer focuses only on key aspect(like policy)
SDN Controller Information Management
One-click deployment
Write Maple program in web-based editor easily
Web-based UI for real network operation
Mininet based tools for network test
Automatic generate visualized trace tree

## Slide 5: Maple(high-level, all-layer programming)
High-level, completely south-bound agnostic, cross-layer (L2-L7) programming
Programmer sees (logically) each and every packet
Integrated access control supporting per-user or role based programming
1. private static final String[] H12_TAP = { H1, "openflow:1:2", "openflow:2:1" }​
2. private static final String[] H12_ONE = { H1, "openflow:1:2", "openflow:2:3", "openflow:4:1" }​
3. private static final String[] H12_TWO = { H1, "openflow:1:3", "openflow:3:2", "openflow:4:1" } ​
4.​void f(Packet pkt) {​
5. int srcIP = pkt.srcIP; int dstIP = pkt.dstIP;​
6. String flowId = computeFlowId( srcIP, dstIP, pkt.srcPort, pkt.dstPort, pkt.protocol );​
7. if ( srcIP == H1 && dstIP == H2 ) {​
8. FlowMetadata fm = getFlowMetadata(flowId); ​
9. if ( fm == null ) { ​
10. pkt.addRoute( H12_TAP );​
11. pkt.addRoute( H12_ONE );​
12. } else if ( isVideo( getUri( fm ) ) ) {​
13. pkt.addRoute( H12_TWO );​
14. } else pkt.addRoute( H12_ONE );​
15. } else if ( srcIP == H2 && dstIP == H1 ) {​
16. …​
17. } else pkt.addRoute( Route.drop );​
18. }​
Per-packet
programming
model
South-band
agnostic
Meta header to
control cross
layers
Does not specify anything on flow tables!

## Slide 6: FAST(automation function store)
Automatic execution MapleApp dependency tracking
Automatic cleanup, re-execution MapleApp (intent ++)
Host generic network functions

## Slide 7: DEMO(Realizing Super SDN Programming using OpenFlow & Bro)
S1
S3
S2
S4
Client1
Server
Bro
Controller
1:IDE writes MapleApp and Bro programs
2:IDE deploys MapleApp and Bro programs
Client2
3:Client1 sends a request for a word file at the Server
4:Client2 sends a request for an mp4 file at the Server
MapleApp.java
http.bro
Step of Demo（Firstly, Start an HTTP server at the Server ）:
When user want to get different type file, Bro can got L7 info->controller. FAST can trace data dependence and re-execute Maple->get new path to send different file.
Set default datapath:S1->S2->S4, Make Bro can get http information.
It’s work!
Notes: Demo explain:
1. WebIDE can quick programming with Maple and FAST.
2. Each and every packet can execute by MapleAPP.
3. Maple can handle cross-layer programming. Such as : SrcIP in L2, GetUri in L7.
4. MAple can completely south-bound agnostic.
5. FAST can automatic trace data dependence, If any change, FAST can re-execute the MapleApp.
6.Controller can deploy all flow rule and switch flow table.

## Slide 8: Summary
Powerful state of the art, generic tools to substantially simplify SDN programming
Low-level, complex, limited (L2-L4) OpenFlow rule programming
Programmer can define only at flow level
Specific access control allowing only hosts partition
Complex, manual tracking of execution dependency
Manual cleanup, re-execute
Designed directly on raw data store
Complex, manual maven programming
Before
High-level, completely south-bound agnostic, cross-layer (L2-L7) programming
Programmer sees (logically) each and every packet
Integrated access control supporting per-user or role based programming
Automatic execution dependency tracking
Automatic cleanup, re-execution (intent ++)
Host generic network functions
Web-based automatic generation of projects
Programmer focuses only on policy decision.
Now
Manual odl programming
Low level, limited programming model
Raw data store
WebIDE
Maple
FAST

## Slide 9: Thank You